## Slide 1: HERON Workshop Examples
A case-by-case training in running HERON
INL/MIS-22-65661

## Slide 2: Learning by Example
HERON cases from basic to complex
Exercises, follow-alongs
Examples found in HERON/tests/workshop/htse

## Slide 3: HERON Calculation Flow
HERON:
Workflow Writer
RAVEN Outer
Ensemble:
SynthHist
Dispatch
TEAL
RAVEN Inner
Sample
Postprocess
Optimize Capacity
Portfolio
DispatchManager
Optimize Dispatch
Loop Structure
Sample
Sample
Sample
Sample
E[NPV]
DispatchManager
For each year …
For each cluster …
… optimize dispatch
Time History
Optimization Window
Technology
Characteristics

## Slide 4: Example 1
As Simple As They Come

## Slide 5: Starter Case
Components
  NGCC (natural gas electricity generator)
  Import (imports electricity from external)
  Grid (demand to be met)
Objective
  How big should the NGCC be built to minimize costs?

## Slide 6: Starter Case
Guiding Physics/Economics (Drivers)
  Grid
    fixed demand to be met
  NGCC
    Capital cost for sizing
    Variable cost for dispatching
  Import
    Variable cost (expensive!) for providing electricity

## Slide 7: Translating to HERON
See HERON/tests/workshop/simple/heron_input.xml
Case
  Global information about the problem
  Time shape, discount rates, solvers, etc.
Components
  Technical and economic properties of each component
  Produces and Demands
  Dispatch: Independent and Fixed
DataGenerators
  Synthetic History Data Source

## Slide 8: Component by Component
Grid
Technical Specs | 
Action | Demands electricity
Flexibility | Fixed (must meet demand)
Capacity | From synthetic time series (trained separately)
Economics | 
None | System is regulated market; minimize cost to meet demand, so there is no sales profit at the grid

## Slide 9: Component by Component
NGCC
Technical Specs | 
Action | Produces electricity
Flexibility | Independent (0 to [Capacity] each hour)
Capacity | Variable from 10 to 60 GW (note: units not included)
Economics | 
Capex | Overnight cost of building component per GW installed
Variable O&M | Operation and fuel costs per GWh produced
Notes: Talk about ValuedParams, Fixed Value
Depreciation, DiscountRate
resource conventions

## Slide 10: Component by Component
Import
Technical Specs | 
Action | Produces electricity
Flexibility | Independent (0 to [Capacity] each hour)
Capacity | Large number (infinite source)
Economics | 
Variable O&M | Operation costs per GWh imported

## Slide 11: Consider the Case
Why Import?
  Why not just have NGCC?
  If NGCC not enough to meet demand, solve “fails”
    This doesn’t provide useful feedback to optimizer; it doesn’t know what’s wrong
    Instead, provide large incentive to meet demand with NGCC
    Example:
GW
NGCC
Import
Demand

## Slide 12: Demand
Stochastically Trained
Based on NYISO projections from EPRI
See INL/EXT-21-65473,
“A Technical and Economic Assessment of LWR Flexible Operation for Generation/Demand Balancing to Optimize Plant Revenue”, Dec 2021

## Slide 13: Running the Case
Sweeping over 6 build sizes
  ~90 seconds, results may vary by OS, machine
Things to look at (see following slides):
  Screen Output
  1_simple_o/sweep.csv (spreadsheet) progress
> /path/to/heron heron_input.xml
> /path/to/raven_framework outer.xml

## Slide 14: Things to Look At While Running
Screen Output: How To Read the Matrix
  Sweep Sample
    Submission of each individual parametric sweep value

## Slide 15: Things to Look At While Running
1_simple_o/sweep.csv – progress of the sampler
case name
outer
sampling record
Component Sizes
(opt variables)
Mean NPV
(objective)
Statistics
Inflection Point

## Slide 16: Converting to Optimization
Converting Input
  Change <mode> to opt
  Swap from <sweep_values> to <opt_bounds>
    Use sweep results to establish bounds
Optimization requires many more “outer” samples!
  ~90 minutes for this case to converge
    Time may vary by OS, machine
  ~250 iterations

## Slide 17: Running the Case
Optimizing size (takes some time!)
Things to look at (see following slides):
  Screen Output
  1_simple_o/opt_soln_0.csv (spreadsheet) optimizer progress
> /path/to/heron heron_input.xml
> /path/to/raven_framework outer.xml

## Slide 18: Things to Look At While Running
Screen Output: How To Read the Matrix
  Accepted Sample
    This means a new optimal point has been found!

## Slide 19: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rejected Sample
    This means the new proposed opt point is worse than the old opt point
    Reasons: inaccurate gradient, too large step, no better points nearby
    Happens frequently, especially near the end

## Slide 20: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rerun Sample
    Return to best-so-far opt point and rerun the gradient, cut step size
    Helps to resolve two reasons for rejecting proposed opt points

## Slide 21: Things to Look At While Running
1_simple_o/opt_soln_0.csv – progress of the optimizer
case name
outer
optimization record
Optimizer Steps
(sets of samples)
Status of each step
Accepted: improvement!
Rejected: went too far
Rerun: re-check gradient
Component Sizes
(opt variables)
Mean NPV
(objective)
Note our losses are getting smaller!

## Slide 22: Now that it’s done …
Things to look at (see next slides)
  opt_soln_0.csv
    filter opt CSV by “accepted” to see acceptance path
    final solution is the last “accepted” point in the CSV
  opt_path.png
    visualization of opt_soln_0.csv
  screen output

## Slide 23: Things to look at now that it’s done
Screen Output
Summary of optimizer status
  Trajectory that found best point
  Objective value
  Opt Vars values
opt var
objective

## Slide 24: Things to look at now that it’s done
1_simple_o/opt_soln_0.csv
“final” point is solution
  243 iterations is low (good!)
opt var
objective

## Slide 25: Things to look at now that it’s done
1_simple_o/opt_path.png
Messy plot
Many plots are bad
    but some are useful
Not intended for report quality
    Indicative of process
capacities
(opt vars)
towards the end only small changes
E[NPV]
(objective)
most optimization happens in the first
few time steps

## Slide 26: Wrap up Example 1
That’s it!
Takeaways:
  3-unit problem, single resource
  Setting up feasible problems
  Running and observing HERON runs
  Viewing results