## Slide 1: HERON Demonstration Part 1: Simple System
Elizabeth Worsham
Paul Talbot
Idaho National Laboratory
Lise Meitner Program 2
October 26 , 2023

## Slide 2: Learning by Example
HERON cases from basic to complex
Exercises, follow-alongs
Examples found in HERON/tests/workshop/
  This case can be found in workshop/simple/

## Slide 3: Set up HERON
module load raven
cd /scratch/<username>
git clone https://github.com/idaholab/raven.git
cd raven
git submodule update --init plugins/HERON
git submodule update --init plugins/TEAL
./scripts/install_plugins.py -s HERON
./scripts/install_plugins.py -s TEAL
cd plugins/HERON/doc/workshop/LM2Tutorial/simple
heron heron_input.xml
raven_framework outer.xml

## Slide 4: HERON Calculation Flow
HERON:
Workflow Writer
RAVEN Outer
Ensemble:
SynthHist
Dispatch
TEAL
RAVEN Inner
Sample
Postprocess
Optimize Capacity
Portfolio
DispatchManager
Optimize Dispatch
Loop Structure
Sample
Sample
Sample
Sample
E[NPV]
DispatchManager
For each year …
For each cluster …
… optimize dispatch
Time History
Optimization Window
Technology
Characteristics

## Slide 5: Starter Case
Components
  NGCC (natural gas electricity generator)
  Import (imports electricity from external)
  Grid (demand to be met)
Objective
  How big should the NGCC be built to minimize costs?

## Slide 6: Starter Case
Guiding Physics/Economics (Drivers)
  Grid
    fixed demand to be met
  NGCC
    Capital cost for sizing
    Variable cost for dispatching
  Import
    Variable cost (expensive!) for providing electricity

## Slide 7: Translating to HERON
See HERON/doc/workshop/LM2Tutorial/simple/heron_input.xml
Case
  Global information about the problem
  Time shape, discount rates, solvers, etc.
Components
  Technical and economic properties of each component
  Produces and Demands
  Dispatch: Independent and Fixed
DataGenerators
  Synthetic History Data Source

## Slide 8: Component by Component
Grid
Technical Specs | 
Action | Demands electricity
Flexibility | Fixed (must meet demand)
Capacity | From synthetic time series (trained separately)
Economics | 
None | System is regulated market; minimize cost to meet demand, so there is no sales profit at the grid

## Slide 9: Component by Component
NGCC
Technical Specs | 
Action | Produces electricity
Flexibility | Independent (0 to [Capacity] each hour)
Capacity | Variable from 30 to 50 GW (note: units not included)
Economics | 
Capex | Overnight cost of building component per GW installed
Variable O&M | Operation and fuel costs per GWh produced
Notes: Talk about ValuedParams, Fixed Value
Depreciation, DiscountRate
resource conventions

## Slide 10: Component by Component
Import
Technical Specs | 
Action | Produces electricity
Flexibility | Independent (0 to [Capacity] each hour)
Capacity | Large number (infinite source)
Economics | 
Variable O&M | Operation costs per GWh imported

## Slide 11: Consider the Case
Why Import?
  Why not just have NGCC?
  If NGCC not enough to meet demand, solve “fails”
    This doesn’t provide useful feedback to optimizer; it doesn’t know what’s wrong
    Instead, provide large incentive to meet demand with NGCC
    Example:
GW
NGCC
Import
Demand

## Slide 12: Demand
Stochastically Trained
Based on NYISO projections from EPRI
See INL/EXT-21-65473,
“A Technical and Economic Assessment of LWR Flexible Operation for Generation/Demand Balancing to Optimize Plant Revenue”, Dec 2021

## Slide 13: What is Net Present Value?
The Net Present Value (NPV) is the present-year value of a future cash flow based on a discount (or interest) rate
Used to determine the long-term value of an investment
NPV > 0 | NPV = 0 | NPV < 0
Investment has a positive return | Breakeven | Investment has a negative return
https://corporatefinanceinstitute.com/course/corporate-finance-fundamentals/

## Slide 14: Optimization Basics
Objective function: What outcome are you looking for?
  Y=x^2+1 … Minimize Y by changing X
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
First Evaluation
Y(-0.5)=1.25
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
Second Evaluation
Y(0.1)=1.01
Y(0.1)-Y(-0.5) = -0.2
We are decreasing! Keep going in that direction!

## Slide 15: Optimization Basics, cont.
The algorithm will continue evaluating at different points to find the minimum. If the objective function starts increasing, it will check in the other direction
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
Second Evaluation
Y(0.1)=1.05
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
Third Evaluation
Y(1)=2
Y(1)-Y(0.1) = 0.95
We are increasing! Try the other way

## Slide 16: Optimization basics, cont.
Once it finds a local minimum, the points around it will be evaluated to check that the objective function increases at the values of X around it.
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
Third Evaluation
Y(0.1)=1.05
Y(0)-Y(0.1) = -0.05
This is the minimum!
Chart: 
| -1 | 0 | 1
Y-Values | 2 | 1 | 2
Fourth Evaluation
Y(0)=1

## Slide 17: HERON for Optimization
Converting Input
  Change <mode> to opt
  Swap from <sweep_values> to <opt_bounds>
    Use sweep results to establish bounds
Optimization requires many more “outer” samples!
  ~90 minutes for this case to converge
    Time may vary by OS, machine
  ~250 iterations

## Slide 18: Things to Look At While Running
Screen Output: How To Read the Matrix
  Accepted Sample
    This means a new optimal point has been found!

## Slide 19: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rejected Sample
    This means the new proposed opt point is worse than the old opt point
    Reasons: inaccurate gradient, too large step, no better points nearby
    Happens frequently, especially near the end

## Slide 20: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rerun Sample
    Return to best-so-far opt point and rerun the gradient, cut step size
    Helps to resolve two reasons for rejecting proposed opt points

## Slide 21: Things to Look At While Running
1_simple_o/opt_soln_0.csv – progress of the optimizer
case name
outer
optimization record
Optimizer Steps
(sets of samples)
Status of each step
Accepted: improvement!
Rejected: went too far
Rerun: re-check gradient
Component Sizes
(opt variables)
Mean NPV
(objective)
Note our losses are getting smaller!

## Slide 22: Now that it’s done …
Things to look at (see next slides)
  opt_soln_0.csv
    filter opt CSV by “accepted” to see acceptance path
    final solution is the last “accepted” point in the CSV
  opt_path.png
    visualization of opt_soln_0.csv
  screen output

## Slide 23: Things to look at now that it’s done
Screen Output
Summary of optimizer status
  Trajectory that found best point
  Objective value
  Opt Vars values
opt var
objective

## Slide 24: Things to look at now that it’s done
1_simple_o/opt_soln_0.csv
“final” point is solution
  243 iterations is low (good!)
opt var
objective

## Slide 25: Things to look at now that it’s done
1_simple_o/opt_path.png
Messy plot
Many plots are bad
    but some are useful
Not intended for report quality
    Indicative of process
capacities
(opt vars)
towards the end only small changes
E[NPV]
(objective)
most optimization happens in the first
few time steps

## Slide 26: Wrap up Example 1
That’s it!
Takeaways:
  3-unit problem, single resource
  Setting up feasible problems
  Running and observing HERON runs
  Viewing results

## Slide 27: HERON Demonstration Part 2: Full IES System
Elizabeth Worsham
Dylan McDowell
Idaho National Laboratory
Lise Meitner Program 2
October 26 , 2023

## Slide 28: Getting Started
Navigate into the IES workshop folder
Open heron_input.xml
  VSCode
  Notepad
  Emacs

## Slide 29: Debug Mode

## Slide 30: System Configuration & Case Information
Project Lifetime | 3 Years
Discount Rate | 8%
Tax Rate | 30%
Inflation Rate | 6%
ARMA Samples | 25
Component | Capital Expenditure | Fixed O&M
Nuclear Power Plant (NPP) | $12.8M / MW | 
Wind Turbine | $1.3M / MW | $15,000 / MW
Steam Turbine | - | -
High Temperature Steam Electrolysis (HTSE) | $1.9M/MW | $131,333 /MW
Hydrogen Storage | $1.2M/MW | -
Component | Sales Price
Energy Grid Market | $100 / MW
Hydrogen Market | $8 / Kg
images: Flaticon.com

## Slide 31: Debug Mode Continued…

## Slide 32: Sweep Run
Now let’s go ahead and run an entire sweep case:

## Slide 33: Sweep Run Continued…
There should now be a sweep.csv inside of IES_o/
What system configuration provides the highest mean NPV?

## Slide 34: Hints… 20 Year Investment Horizon
You may also want to change the lifetime nodes to last longer than 5 years:

## Slide 35: Hints… Adding Lithium-Ion Battery
Start by copying the H2 Storage Node and then modifying as necessary

## Slide 36: Hints… Optimization Runs
Change all sweep_values to opt_bounds
Note: This may take a long time to run!
To see pre-run optimization results, look in: gold/IES_o/opt_soln_0.csv

## Slide 37: What We Didn’t Cover
Custom Dispatching Strategies
  Price-Taker vs. Price-Maker
Custom User-Defined Functions
Control Strategy for Storage
Different HERON Workflows:
  DISPATCHES
  MOPED
We are Open-Source!
  Open an issue on repository
  Contribute meaningful code changes