## Slide 1: HERON Wind/NPP Case
Gabriel J. Soto Gonzalez, Paul Talbot
Modeling and Simulation Engineer
Idaho National Laboratory
FORCE Overview and Training
April 4-6, 2023

## Slide 2: Outline
Wind and Nuclear Power Plant (NPP) Case
  Basic schematic of Integrated Energy Systems (IES) components
  Market and Weather scenarios
  Holistic Energy Resource Optimization Network (HERON) Workflow
  HERON Input script
  Running HERON simulation in Debug Mode
  Running HERON simulation in Sweep Mode
Adding Arbitrage

## Slide 3: NPP and Wind
Stronger Together (Sometimes)

## Slide 4: Basic Schematic of IES
Nuclear Power Plant
  Can flex from 0%–100% of rated capacity
Wind Farm
  Also has rated capacity, but varies based on wind speeds
    Capacity factor taken from synthetic histories
Electricity Grid
  Demand
    also taken from synthetic histories
  External Market (Source/Sink)

## Slide 5: Basic Schematic of IES
Given:
  IES (NPP + Wind Farm)
  Market and Geographic Region
Need to find:
  Capacities
  Dispatch strategies
Goal(s):
  Satisfy demand
  Minimize costs/maximize profits (net present value [NPV])
Recall:
  Load profiles and weather contain uncertainty
  Uncertainty represented using synthetic time histories (Auto-Regressive Moving Average [ARMA])

## Slide 6: Market and Weather Scenarios
Normally, pre-HERON steps include training an ARMA model
  Some RAVEN-trained models included
NYISO data for Load, Wind, Solar
  Load: [GW]
  Wind, Solar: [unitless fraction]
HERON\tests\integration_tests\ARMA\NYISO\Data_0.csv

## Slide 7: Market and Weather Scenarios
ARMA is trained by segmenting full dataset
1 year of data broken down into:
  2 representative clusters
  each 24 hours long
These are parameters decided by the users, kept simple here
HERON\tests\integration_tests\ARMA\NYISO\Data_0.csv

## Slide 8: HERON Workflow
All the hard work has already been done!
From our given ARMA, synthetic histories will:
  Contain a single year
    Contain two clusters per year
      Contain three signals per cluster (Load, Wind, Solar)
      Contain 24 time points per signal
  For a multi-year simulation, HERON can repeat yearly data

## Slide 9: HERON Workflow
Two-stage optimization or sweep:
  Outer: optimizing component capacities using RAVEN Gradient Descent
  Inner: optimizing dispatch of resources using Pyomo and requested solver
    GNU Linear Programming Kit [glpk]
    Coin-or Branch-and-cut [cbc]
    Interior Point Optimizer [ipopt]
Modified from:
A. Epiney, C. Rabiti, P. Talbot, A. Alfonsi, “Economic analysis of a nuclear hybrid energy system in a stochastic environment including wind turbines in an electricity grid” Applied Energy (2020)

## Slide 10: HERON Workflow

## Slide 11: HERON Input Script
Case
num_arma_samples = 20
  20 inner samples used to get expected value of metric (NPV) in Outer
ProjectTime= 3
  Each inner sample simulates 3 project years
<time_discretization>
  Each cluster/segment has 24 time steps
NOTE: clusters/segments automatically read from ARMA
HERON\tests\workshop\wind\heron_input.xml

## Slide 12: HERON Input Script
<capacity>
  This is the rated capacity of the Wind Farm
  Currently, we sweep through some values
    Can be fixed, opt, etc.
<capacity_factor>
  Actual usage of capacity per unit time
  Using synthetic histories
Components: Wind
HERON\tests\workshop\wind\heron_input.xml

## Slide 13: NPP and Wind
Let’s run some simulations!

## Slide 14: Running in Debug Mode
Uncomment <debug> line
  Note that this overrides some parameters
    Only using 1 sample
    Only using 1 year
Change debug values!
  HERON only use these in debug mode, overrides sweep values
HERON\tests\workshop\wind\heron_input.xml

## Slide 15: Running in Debug Mode
Run HERON, then outer.xml:
Things to try in debug mode:
  Wind = 0; NPP = 20
  Wind = 10; NPP = 20
  Switch NPP to dispatch=“independent” or dispatch=“fixed”
Pause here – Check Network plot!
HERON\tests\workshop\wind\heron_input.xml

## Slide 16: Running in Debug Mode
Run HERON, then outer.xml:
Things to try in debug mode:
  Wind = 0; NPP = 20
  Wind = 10; NPP = 20
  Switch NPP to dispatch=“independent” or dispatch=“fixed”
HERON\tests\workshop\wind\network.png

## Slide 17: Running in Debug Mode
Stochastic History for Single Cluster
Dispatch of Electricity
Wind = 0GW
NPP = 20GW, independent dispatch
HERON\tests\workshop\wind\npp_wind_o

## Slide 18: Doing a Full Sweep
Run HERON, then outer.xml:
Things to change:
  Comment out the <debug/> line
  Input desired sweep values for:
    Wind Capacities
    NPP Capacities
Pause here
HERON\tests\workshop\wind\heron_input.xml

## Slide 19: Doing a Full Sweep
Zoomed-in plot
Results!
Chart: 
| 0 | 20 | 40 | 60
0 | -330461797249 | -3392682215.88 | 5379571331.26 | 1320752.3636
10 | -232247733680 | 3986704370.34 | 4412665081.95 | -977368147.524
30 | -99596722067.3 | 4484587753.47 | 2229240923.89 | -3171978867.43
50 | -67875678954.6 | 3364569392.33 | -253021111.323 | -5689697567.88
70 | -53324085327.1 | 1043246108.34 | -2881517513.04 | -8278161852.2
90 | -46110884841.3 | -1545823667.55 | -5473789414.37 | -10871265196
Chart: NPP Capacity (GWe)
| 0 | 20 | 40 | 60
0 | -330461797249 | -3392682215.88 | 5379571331.26 | 1320752.3636
10 | -232247733680 | 3986704370.34 | 4412665081.95 | -977368147.524
30 | -99596722067.3 | 4484587753.47 | 2229240923.89 | -3171978867.43
50 | -67875678954.6 | 3364569392.33 | -253021111.323 | -5689697567.88
70 | -53324085327.1 | 1043246108.34 | -2881517513.04 | -8278161852.2
90 | -46110884841.3 | -1545823667.55 | -5473789414.37 | -10871265196

## Slide 20
After running in debug mode and getting a coarse look via sweep runs, might be time for an optimization run
  Will take a while depending on computation resources
  best to do on your own or on High Performance Computing (HPC) machines
Fun things to toggle—How do these affect NPV?:
  Project time > 3 years
  Project time > component lifetimes
  Add depreciation to components

## Slide 21: NPP and Wind With Storage
Even Stronger with Arbitrage!

## Slide 22: Basic Schematic of IES
Nuclear Power Plant:
  Nuclear Reactor
    Is now decoupled from electricity generation
    Produces heat that can be converted to electricity
  Turbine
    Converts heat into electricity via a transfer function (η= 0.33)
Thermal Energy Storage (TES)
  Storage unit that can charge with heat and discharge via some dispatch strategy

## Slide 23: Basic Schematic of IES
Wind Farm
  Also has rated capacity, but varies based on wind speeds
    Capacity factor taken from synthetic histories
Battery
  Storage for electricity resource
Electricity Grid
  Demand
    also taken from synthetic histories
  External Market (Source/Sink)

## Slide 24: Basic Schematic of IES
Given:
  IES (NPP + TES + Wind Farm + Battery)
  Market and Geographic Region
Need to find:
  Capacities
  Dispatch strategies
Goal(s):
  Satisfy demand
  Minimize costs/maximize profits (NPV)
Recall:
  Load profiles and weather contain uncertainty
  Uncertainty represented using synthetic time histories (ARMA)

## Slide 25: HERON Input Script
Turbine converts heat to electricity
  Linear transfer rate – efficiency
  Dispatch is “dependent”
    Capacity large enough to take in NPP and TES production
Reactor generates heat
  Keeping previous costs ($/GWe)
  Efficiency used as multiplier (GWt/GWe)
Efficiency
Efficiency
Different resource
HERON\tests\workshop\wind\heron_input_storage.xml

## Slide 26: HERON Input Script
TES stores heat
  Assuming only CAPEX (capital expenditures) cost
    $30/MWt
Battery stores electricity
  Assuming only CAPEX (capital expenditures) cost
    $151/MWe
HERON\tests\workshop\wind\heron_input_storage.xml

## Slide 27: Running in Debug Mode
Run HERON, then outer.xml:
Things to try in debug mode:
  Component sizes:
    Wind = 30; Reactor = 20
    TES = 30; Battery = 30
  Switch Reactor to dispatch=“independent” or dispatch=“fixed”
Pause here – Check Network plot!
HERON\tests\workshop\wind\heron_input_storage.xml

## Slide 28: Running in Debug Mode
Run HERON, then outer.xml:
Things to try in debug mode:
  Component sizes:
    Wind = 30; Reactor = 20
    TES = 30; Battery = 30
  Switch Reactor to dispatch=“independent” or dispatch=“fixed”
HERON\tests\workshop\wind\network.png

## Slide 29: Running in Debug Mode
Stochastic History for Single Cluster
Dispatch of Heat and Electricity
HERON\tests\workshop\wind\npp_wind_storage_o
Wind = 10 Gwe
Reactor = 20 GWt (independent dispatch)
TES = 5 GWt
Battery = 2 GWe

## Slide 30: Doing a Full Sweep
Run HERON, then outer.xml:
Things to change:
  Comment out the <debug/> line
  Input desired sweep values for:
      Wind Capacity
      Reactor Capacity
      TES Capacity
      Battery Capacity
HERON\tests\workshop\wind\heron_input_storage.xml

## Slide 31: Doing a Full Sweep
Some results from multi-dimensional results
Try different sweep values!
  Fixed Reactor output
  Higher Grid Demand
Chart: Wind = 0 GWe Reactor = 50 GWt
| 0 | 10
0 | 4496265356.36 | 6026865670.84
5 | 6610466384.07 | 7901349762.03
Chart: Wind = 15 GWe Reactor = 0 GWt
| 0 | 10
0 | -183719830186 | -183848761340
5 | -183619105056 | -183943693181
Chart: Wind = 15 GWe Reactor = 50 GWt
| 0 | 10
0 | 6447175377.14 | 7330587020.35
5 | 7219639968.64 | 7777749490.49